## Slide 1
VOLTHA 2.8 Techinar
July 14, 2021 | 9am PDT
Andrea Campanella, Girish Gowdra, Hardik Windlass, Matteo Scandolo
ONF

## Slide 2: Outline
SEBA RD 2.0 and VOLTHA Architecture, project state and deployments
VOLTHA Long Term Support Release and Strategy
VOLTHA 2.8 release
  ETCD Persistence at scale
  Multi User Network Interface (multi-UNI) Support
  IETF Bandwidth profile and 5 TCONT Selection
  Performance Measurements and Alarms
  Platform stabilization (ONOS 2.5, Distroless images, bug-fixes, OMCI channel, voltctl, ONU SW image update)
  Testing and Certification of new OLT
VOLTHA 2.9 Roadmap
Q/A

## Slide 3: SEBA Reference Design Architecture
SEBA is a lightweight platform for development of solutions for carrier broadband access
SEBA RD v 2.0:
Disaggregated Broadband Network Gateway (BNG)
Per-OLT VOLTHA Stack Model for Scaling
Detailed NBI APIs
Device Management (DM)
Seba RD 2.0 is Released SEBA RD 2.0 Webinar

## Slide 4: SEBA 2.0 Exemplar Architecture
BNG-UP
Core
Docker
Kubernetes
Helm
Network Edge Mediator (NEM)
Edge orchestration and FCAPS micro-services
SEBA POD
ONAP
Operator OSS/BSS
Local adaptor
VOLTHA
Compute
servers
SOFTWARE STACK
HARDWARE
SDN Controller - ONOS
OpenFlow
P4Runtime,
gNMI/OpenConfig
VOLTHA apps PON/OLT control
TRELLIS apps
Fabric control
BNG-CP apps
Subscriber control
Whitebox OLT
Whitebox OLT
whitebox switch
whitebox switch
Stratum
ONU
RG
PON
Focus on access: ONOS and VOLTHA

## Slide 5: VOLTHA: Virtual OLT Hardware Abstraction
VOLTHA core
Whitebox OLT
OpenOLT
Adaptor
BAL
SDK(s)
OpenOLT driver/agent
ONL
ONIE
ONOS 1
Client
(eg. OFAgent)
kafka
ONU
ONU
ONU
ONOS 1
ONOS
Common Control & Management for PON networks (OLTs and ONUs)
Different brands of OLTs and ONUs
Multiple services and operator workflows (ATT, TT, DT)
Device Management Interface for non datapath operations (e.g olt software upgrade)
Scale deployments (10 Stack with 10240 subscribers with the same infra)
Software update (VOLTHA and ONUs)
Hardware, scale, soak testing
Etcd
kafka
Openflow
Device Management Interface
OpenONU
Adaptor
OMCI
VOLTHA 2.7 Webinar https://docs.voltha.org/master/release_notes/voltha_2.7.html
Notes: OLT is abstracted with olt-adapter
ONU is abstracted with onu-adapter
ONUs + OLT are abstracted to the SDN controller as a switch
A constellation of OLT and ONUs is exposed via a single SDN controller

## Slide 6: VOLTHA Deployments with Operators
Voltha is in production with live customers:
Deutsche Telekom (DT) as part of the A4 project
  https://www.telekom.com/en/media/media-information/archive/deutsche-telekom-s-access-4-0-platform-goes-live-615974
Turk Telekom (TT)
  https://www.aa.com.tr/en/science-technology/turkish-gsm-giant-makes-global-move-in-network-tech/2126349

## Slide 7: VOLTHA Long Term Support Releases
Long Term Support means that throughout the lifetime of a release there is a commitment to update, patch and maintain the software (more info)
VOLTHA is a stable feature-rich project and has reached a level of maturity where it can be meaningfully used by others as part of their product or solution.
VOLTHA 2.8 is the first Long Term Support release of the project.

## Slide 8: VOLTHA Long Term Support Releases
VOLTHA Long Term Support process is as follows:
18 months support with bug fixes and testing
LTS releases are 18 months apart.
6 month release cycles
Two interim releases between LTS versions.
Bugfixes will be backported to LTS (if applicable) from master and interim release.
LTS gives operators and users more confidence and attracts more users
“We applaud the ONF VOLTHA Community for this milestone achievement. With carrier grade VOLTHA solutions being deployed in production, Network Disaggregation has become a reality. We are looking forward to continuing this fruitful community collaboration.” Manuel Paul, Deutsche Telekom’s Product Owner for VOLTHA development.

## Slide 9: ETCD Persistence at scale
VOLTHA storage through ETCD (pre 2.8) had issues in space occupancy, write speed and use of persistent storage with upstream BITNAMI Charts.
ETCD 6.2.5
Compacted technology profile instances
Removal of flows storage in the rw-core.
Openolt adapter read-through cache
ETCD connection pool in voltha-lib-go
Optimization of stored attributes
Automatic compaction and defragmentation
Use of nVME disks
Lowered disk space usage by 80%, faster bring-up and provision time of 1024 ONUs (2 mins) with persistence enabled for failure scenarios

## Slide 10: Performance Measurements
ANI-G Test message support to fetch rx/tx power at the ONU
ONUi-PON and ONUi-GEMj counters
Extended Ethernet PM counters
Ethernet Bridge History
GEM Port History
FEC History
OLT Transceiver data via DMI
Collaboration with operators to ensure better network visibility, debugging and live analysis

## Slide 11: IETF Bandwidth profile
Extends previous MEF definition that used EIR/EBS (excess information rate, burst size) and AIR (assured information rate). If we define EIR, CIR, AIR we will calculate PIR =CIR + EIR + AIR.
{ "id": "DT_downstream_default_bw_profile", "pir": 1168192, "pbs": 0, "cir": 0, "cbs": 0, "gir": 0 }
Added IETF representation of the Bandwidth profile:
PIR /PBS (peak information rate, maximum bandwidth)
CIR/CBS (committed information rate)
GIR (guaranteed bandwidth)

## Slide 12: 5 TCONT Selection
5 Tcont type selection:
Two meter-bands with burst size = 0 (Tcont type 1, PIR=GIR)
One meter-band with burst size = 0 (Tcont type 1, only GIR is specified)
Two meter-bands with burst size > 0 (Tcont type 2 / Tcont type 3, PIR=CIR / PIR > CIR)
One meter-band with burst size > 0 (Tcont type 4, only PIR)
Three meter-bands (Tcont type 5, PIR > CIR + GIR)
Fine grained quality of service (QoS) for each subscriber

## Slide 13: Multi User Network Interface (multi-UNI) Support
Use all use network interface (UNI) ports of an ONU
all ports are active and enabled in VOLTHA and ONOS
Capability to provision subscribers on all UNI ports
different Bandwidth profiles for ONUs and OLTs
support for all workflows and multi-tcont
Mask for amount of enabled ports.
Support in BBSIM
VOLTHA core
ONOS
OpenONU
Adaptor
Fully leverage ONU/ONT Device Capabilities and expand service capability at the same cost

## Slide 14: Platform stabilization
ONOS 2.5 LTS
Expanded ONU software upgrade capability
  Retrieval of image specifics via OMCI of the images from the device
  Separation of download/activate/commit APIs
  Time optimization
OMCI channel
  message send/receive failure handling
  retry mechanisms in openonu adapter
Voltctl extensions
  Multi-stack support
  Groups list
  Retrieve of Performance Metrics
Distroless and non root docker images for production deployment security
Bug fixes

## Slide 15: Turk Telekom Testing
Expanded Turk Telekom hardware tests from 5 to 19, including error and failure scenarios
Disable/Enable ONU
Disable/Delete OLT
Open-olt, Open-onu, Rw-core, Of-agent Restart
Delete/Re-add (reprovisioning) Subscribers
ONU and OLT Physical and Soft Reboot
All done on XGSPON whitebox OLT with different ONU brands and multiple technology profiles for different services needs
Notes: OLT is abstracted with olt-adapter
ONU is abstracted with onu-adapter
ONUs + OLT are abstracted to the SDN controller as a switch
A constellation of OLT and ONUs is exposed via a single SDN controller

## Slide 16: VOLTHA+ONOS 2.8 Testing
New 2.8 Tests
Multi-UNI Testing
Performance Metrics (ANI-G)
Multi-Tcont testing
Updated ONU sw upgrade
Automated Soak testing
OMCI Chaos Monkey
Nightly scale and 180+ Hardware tests
Jenkins view for 2.8 Tests
https://jenkins.opencord.org/view/VOLTHA-2.8/
Notes: OLT is abstracted with olt-adapter
ONU is abstracted with onu-adapter
ONUs + OLT are abstracted to the SDN controller as a switch
A constellation of OLT and ONUs is exposed via a single SDN controller

## Slide 17: Continuous Certification -- Radisys 3200G
VOLTHA 2.8 adds the Radisys 3200G GPON OLT to the Certified Hardware
whitebox OLT
32 GPON ports
openolt agent and adapter
More info: https://radisys.com/connectopenbroadband/olts
Notes: OLT is abstracted with olt-adapter
ONU is abstracted with onu-adapter
ONUs + OLT are abstracted to the SDN controller as a switch
A constellation of OLT and ONUs is exposed via a single SDN controller

## Slide 18: Continuous Certification
Operator’s Procurements is based on successful ONF certification https://opennetworking.org/continuous-certification-program/
180+ nightly Tests certify several HW:
Edgecore ASFVOLT16 (XGSPON)
Edgecore ASGVOLT64 (GPON)
Radisys 3200G (GPON)
Adtran SDX 6320 (GPON) -- in progress
Sercomm FG1000 (GPON ONU)
Edgecore 7712 (Agg switch)
Edgecore 6712 (Agg Switch)
ONF Marketplace:
https://opennetworking.org/marketplace/?_product_project=voltha
Notes: OLT is abstracted with olt-adapter
ONU is abstracted with onu-adapter
ONUs + OLT are abstracted to the SDN controller as a switch
A constellation of OLT and ONUs is exposed via a single SDN controller

## Slide 19: 2.8 Accomplishments
ETCD Persistence at scale with ETCD 6.2.5 and upstream BITNAMI charts
Multi User Network Interface (multi-UNI) Support with testing
New IETF Bandwidth profile format to be compatible with more OSS/BSS
5 TCONT Selection to support all bandwidth/Qos requirements
Extended Performance Measurements and Alarms
Platform stabilization (ONOS 2.5, Distroless images, bug-fixes, OMCI channel, voltctl, ONU SW image update)
Expanded Testing suite, especially TT and alarms/OMCI
Certification of new Radisys 3200G OLT
https://docs.voltha.org/master/release_notes/voltha_2.8.html
Notes: OLT is abstracted with olt-adapter
ONU is abstracted with onu-adapter
ONUs + OLT are abstracted to the SDN controller as a switch
A constellation of OLT and ONUs is exposed via a single SDN controller

## Slide 20: VOLTHA 2.9 Roadmap
gRPC migration from KAFKA for inter VOLTHA services communication
ONU Adapter Code Modularization and Channel based flow config
TT multicast test and IGMP at scale
Containers resource limits
Alarms and PMs (LOS and Loss of PLOAM)
ADTRAN and Radisys OLT certification
Extend multicast, IGMP, multi-UNI tests
BAL upgrade (possible)
MPLS support (possible)
Notes: OLT is abstracted with olt-adapter
ONU is abstracted with onu-adapter
ONUs + OLT are abstracted to the SDN controller as a switch
A constellation of OLT and ONUs is exposed via a single SDN controller

## Slide 21: SEBA Community
AT&T
Notes: Today we present the work of a large community that includes both operators and vendors

## Slide 22
Thank You
Follow Up Links:
docs.voltha.org
andrea@opennetworking.org
teo@opennetworking.org
girish@opennetworking.org
hardik@opennetworking.org